POWER C SHELL ENVIRONMENT ASSEMBLERS

PROGRAMMERS' WORKSHOP CONFERENCE 5/25/89

by SYSOP JL

There are two 65xx symbolic assemblers which operate in the Power C Shell

environment. In order to use these assemblers you must have Power C from

Spinnaker Software. Then, using one of these assemblers, you can assemble

your own machine language functions callable from C or even write stand

alone ML programs with the features afforded by the assemblers and the

Power C linker.

The two assemblers are ASSM.SH and ASM.SH. The ASSM.SH program is

downloadable from the Programmers' Workshop / C Language / Source

library. ASM.SH is part of the Power Assembler package from Spinnaker or

the update to it, Buddy V10 available from the program author, Chris

Miller. ASSM.SH runs under the C64 version of Power C while ASM.SH runs

only under the C128 version of Power C.

FEATURES

CASSM is a fairly basic symbolic assembler. Source code is SEQ PETASCII

files on disk, typically created with the Power C editor. Its main

feature is that it produces relocatable .obj output files on disk which

are then linked using the Power C Linker. The linker is used to

optionally specify a load address and to link other .obj files together,

producing a loadable or executable file.

ASM is a full featured symbolic assembler. Source code is SEQ PETASCII on

disk or RAMDISK, typically created by the Power C editor or by the EBUD

editor (ED128) which is part of the "Buddy" system (Power Assembler).

Assembler features are essentially the same as the family of Buddy

assemblers including temporary labels, long labels, conditional assembly,

offset assembly and user definable macros for Buddy V10. Like ASSM it

creates relocatable .obj files that are combined using the Power C Linker

to create loadable or executable disk files.

USES

There are three typical uses for these 65xx assemblers. 1) Modifying

Power C library functions; 2) Creating ML functions for use in C programs

written for Power C; and 3) Creating stand alone ML programs in a modular

fashion. The procedures to follow for each of these purposes are covered

below.

MODIFYING POWER C LIBRARY FUNCTIONS

You may wish to modify Power C library functions for special purposes or

to create new functions closely related to existing library functions.

The steps to do this are as follows...

1.   Use RA.SH (from downloaded file RA.ARC) to disassemble the .obj

library module from one of the Power C disks. The result will be a

ASSM.SH compatible source file on the work disk. This is done in C64

mode using the C64 Power C version, but a C128 library function can

be disassembled in this fashion also.

2.   Use a SEQ file editor (such as ED.SH in Power C) to make the desired

changes. If you are using Buddy's ASM.SH to assemble the file on a

C128 then you also need to make the (minor) source format changes for

compatibility with this assembler. Include notes on the changes made

and reasons for the changes.

3.   Use ASSM.SH or ASM.SH to assemble the modified function. This file

should be written to a work disk other than the Power C library disk

along with the edited source. Now do either of two things to update

the Power C library. Give the new file a different name than the old

file, copy it to the library disk, and update the .l library file

which references it using the LIB.SH program on the Power C disk; or

Rename the old .obj function to something else (to keep it), then

copy the new function to the library disk giving it the same name as

the original function.

4.   Test the revised function thoroughly.

CREATING A NEW ML FUNCTION FOR POWER C

The steps to create a new ML function for use with your Power C programs

are as follows :

NOTE: THROUGHOUT THE FOLLOWING EXAMPLES THE CHARACTER ' (SEMI-QUOTE) IS

USED IN PLACE OF THE UNDERLINE CHARACTER. The Power C editor allows for

the use of this character as part of a label and C functions use it

extensively. However, not all word processors, printers and SEQ file

readers will allow for it printing. Thus the substitution in this text.

This is particularly important to note with regard to explicit

definitions of labels of Power C library functions such as C$FUNCT¤INIT

including the underline character, which are shown here in as

C$FUNCT'INIT.

1.   Write the source code for your ML function using a SEQ file editor

such as the Power C editor or Buddy's EBUD. Documentation for the

ASSM.SH assembler is in the C-ASSM.ARC file. The Buddy ASM.SH

assembler is basically the same as BUD or EBUD except that .BAS,

.ORG, .OFS, and .OBJ pseudo-ops are not allowed. There is no specific

documentation on ASM.SH in the Power Assembler package, but Buddy V10

from Chris Miller includes enough info to use it. The following

machine specific info may be helpful...

- C64 Power C : The C64 Power C parameter stack starts at $033c and

moves upwards. Zero page function work area is available at $4b-$74.

Upon entering your function, to get access to parameters passed from

the C function call, include the following code...

jsr c$funct'init    ; get parameter stack index

stx temp            ; in case you need it again

lda param'stack,x   ; $033c indexed by the parameter stack pointer

Parameters will be passed in the internal format defined in the Power

C manual; INT parameters and pointers as 2 byte parameters in

low-byte / high-byte order; long int, short and char are converted to

INT; float and double passed as float with 5 bytes per value; etc.

Using ASSM.SH, any label, including the callable function name, that

is to be accessed from C or other ML functions must be defined in a

.def statement somewhere in the source code. These identify the

labels in your ML for which the linker needs your .obj file to

resolve.

.def internal'label,internal'label,...

ASSM.SH also requires that you define labels that you use which are

external to your function. This is done with the .ref pseudo-op.

.ref external'label,external'label,...

For example, if your C function is called from C with BELLS(ch); and

returns with a status byte saved at the static location BELLS'STATUS

then the following code elements would be needed for ASSM.SH...

.ref c$funct'init

.ref c$chkout,c$chrout

.def BELLS, BELLS'STATUS

;

parms = $033c              ; Power C C64 Parameter stack location

bells = *                  ; called from external procedure

jsr c$funct'init   ; get parameter stack index

stx temp           ; save it for return params

lda parms,x        ; get parameter ch in .A

sta bells'status   ; accessible externally

rts

temp    .byte 0            ; local index save

bells'status .byte 0       ; globally accessible static variable

You can return a function value to C by storing it on the parameter

stack at the original X register index offset. In the above example

you could have returned the char value bells'status as a return

parameter to the C call with the following code in place of the sta

bells'status...

ldx temp           ; get the original offset

sta parms,x        ; save the byte (char) return value

lda #0             ; dummy high byte set to zero

sta parms+1,x      ; save it as the high byte of the return

In the C64, BASIC ROM is banked out but I/O and Kernal ROM are

visible. Save your source file with a .A or .ASM extension (for

example, bells.a) to indicate it is an assembler source code file.

- C128 Power C : The C128 parameter stack is at $0400 and moves

upward to $05ff. C programs start at $0600. Zero page temporary work

area is available at $a0. If you need extensive zero page you should

relocate page 0. As with the C64 configuration, a jsr c$funct'init

will return the parameter stack pointer in the X register. Buddy's

ASM.SH assembler requires that labels in your routine that are

intended to be externally referenced be defined with a .ext pseudo-

op. For the example in the C64 info above...

.ext bells,bells'status

This pseudo-op takes the place of the .def pseudo-op in the ASSM.SH

assembler. ASM.SH does not require you to explicitly identify

external references (the .ref pseudo-op in ASSM.SH).

C128 C programs are linked to run in C128 RAM bank 1 with only RAM in

context. To get access to I/O you must save the REU configuration

register ($ff00), set it to I/O in context ($7e), and restore it to

bank 1 RAM ($7f) before returning. Access to the Kernal routines is

through common RAM long JSR's generally called by a jsr to a C

library function with a label c$ plus the Kernal function name.

Disassemble c$kernal.obj for a complete list.

2.   Assemble your new ML function using ASSM.SH (C64) or ASM.SH (C128).

For example, the shell call...

ASSM BELLS.A   or   ASM d:BELLS.A d:BELLS   (d: is the drive)

will load the assembler from the system disk, assemble BELLS.A from

the work disk and save the relocatable object file (linker file) as

BELLS.OBJ to the work disk. ASSM.SH replaces the .A extension of the

source file name with the .OBJ extension when it saves the file.

ASM.SH requires you to give a file name to save the output file to

and it automatically adds a .OBJ to the end of the file name. With

ASM.SH, if you do not specify a output file name the assembler will

run and produce error reports, output listings requested, etc but

will not save the assembled file.

3.   Write a small driver program in C or ML and test your routine.

4.   To link your new routine with a C program, give the relocatable

object file name to the linker after your C compiled object file(s)

have been linked and before the library files. For example...

link

> bellstest.o

> bells.obj

> ^

STAND ALONE ML PROGRAM DEVELOPMENT

The Power C shell environment assemblers may also be used in developing

stand alone ML programs for the C64 or C128. This way you can create

separately assembled, relocatable modules that can be linked with the

Power C linker, LINK.SH. When used in this way you do not have to be

concerned about the C memory configuration or usage. You have complete

control of memory use just as you would with any assembled ML program.

Each assembly module that is separately assembled would have to include

the appropriate .ext, .ref and .def pseudo-ops as discussed above.

One additional thing that is needed by the linker that is not obvious...

a label MUST be defined in one of the program modules as an entry point

when the file is loaded. This beginning execution address must have a

label MAIN and that label must be defined as external by a .ext or .def

pseudo-op. When the linker combines the relocatable object modules

including the one with the MAIN label it will produce a JMP to MAIN at

the load address supplied to the linker. Use the -S option on the LINK

call line to produce the stand alone executable file. This linker command

is documented in the Power C manual. If -S and an address is specified

then that address will be the program load address. Otherwise the program

will be linked to load at the start of BASIC as a load and run program

with a SYS to the start address.

REFERENCE FILES

Here is a list of files in the Programmers' Workshop library which will

be of interest in connection with this topic. All files are located in

the Programmers' Workshop / Software Libraries / C Language library in

either the Source or Utility sections as noted.

File name         Uploader    Date     Sublib  Description

----------------  ----------  -------- ------  --------------------------

cassm64stuff.arc  Mark MM     9/12/88  Source  Example assm src files

cassm.arc         Mark MM     4/14/88  Source  The assm.sh files

asm.sh-info       Mark MM     4/14/88  Source  Text info on using ASM.SH

newshell.arc      Dan B15     2/4/89   Utility C64 C Shell assm src code

ra.arc            Mark MM     9/12/88  Utility C64 C symbolic disassembler