HACKING THE V-1541/Comet64 by Warlock

Grab software here: http://www.wiznet.co.kr/Sub_Modules/en/technical/Download_View.asp?PK_Num=222&page=1&SF_Part=&SF_KeyWord=

Turn on c64 load up v-1541 your Comet64 device should get an IP address.

Run WIZnet configure software see screenshot below. Check box to “Direct IP Search” Enter your Comet64 IP in and click “Search”

Change “Server IP” to match your ftp server.  I am using port 1541 that was what the port was to begin with. Please don’t forget to make that change on your FTP server. Then click “Setting” to save the configuration.

Now you’re ready to setup your FTP server.

Give yourself a username and password nothing to hard remember the c64 keys.

Configure FTP server Port to: 1541

Set a home directory for your newly created user.

OK next reset the C64 you should notice some activity on your ftp log area/display

Load v-1541 from the d64 provided @ commodoreserver.com or diosk provided with your device.

Load “v-1541”,8,1

After load type: sys49152

Next type: New to reset basic

To login to your ftp:
Type LOAD”>user YOURUSERID”,2
Type LOAD”>pass YOURPASSWORD”,2

You should be in your ftp.
The only things I have got to work so far:
LOAD”>CWD DIRNAME”,2 switching directories
LOAD”>MKD DIRNAME”,2 Make directories
LOAD”>RMD DIRNAME”,2 Remove Directories
LOAD”>DELE FILENAME”,2 Delete File
LOAD”>HELP”,2 Display Commands for FTP
Couple other commands work but not loading and or saving files

Other stuff should work but it’s not:
LIST or LS for directory listing
GET File

ENJOY maybe someone can get a little farther than me.